IPV6

high speed networks have fixed header length, another thing that has been removed is controls(checksum). The subnetmask is removed
This type of network improve the flow of the network, thus high speeds.
If transfer fails you must receive again the data, no problems because you have high speed network.
Devices can have multiple ips
DHCP
it needs to assign dynamically the ip to the dte.
It is a server.
It can use reservation we can reserve ip for a defined MAC address.
It doesn’t support multiple address for an interface.
It cannot propagate DNS.
it do not support server communication.
it doesn’t send data an authenticated confirmation.

Dynamic IP assignment
3 protocols:
- RARP
- BOOTP
- DHCP
today only dhcp is used

bootp allows the boot of a machine through network.
It assign ip to the machine, it detect an ip addrss for chine server, boot file name
DHCP’s ip has an expire date.